# LMG 1110

Cape Sherriff Opening

Bucklin B-285-L

Warren B-393-L

# Cruise Data Report

By George Aukon and Kris Merrill

2 Nov 2011 – 1 Dec 2011

Table of Contents

Introduction	1

Archive Data Extraction	2

CD Directory Structure	3

Distribution Contents	4

ADCP	4

Calibration	4

Imagery	4

Data and Science Report	4

XBT	4

XCTD	4

Logsheets	4

Salts	5

Science	5

Maps	5

QC Plots	5

JGOFS Data Set	6

TSG Data files	6

RVDAS	7

Meteorological and Light Data	7

Navigational Data	7

Geophysical Data	7

Oceanographic Data	7

Data File Names and Structures	8

lknu – Knudsen Sonar	8

lnds – Net Depth Sensor	9

lwn1 - Winches	9

lmwx	- Campbell Meteorological DAS	9

utsg – microTSG, Thermosalinograph	10

lrtm – digital Remote Temperature	10

ldflr – Fluorometer, Wetlab ECO	10

loxy - Oxygen	11

lpco – PCO2 system	11

Lguv – Biospherical GUV	12

lsvp -  Sound Velocity Probe in ADCP Transducer Well	13

ladc – ADCP Speed Log	13

lgyr - Gyro	13

lsep – Seapath 330 GPS	14

lgar - Garmin GPS	15

tgps – Trimble Centurion GPS	16

LMG Sensors	18

Shipboard Sensors	18

CTD Sensors	18

MOCNESS Sensors	18

Underway Calibration Sheets	19

Remote Temperature	19

Thermosalinograph	20

Transmissometer	21

Fluorometer	22

PSP	23

PIR	24

PAR	25

Temperature/Relative Humidity	26

Barometer	27

GUV	28

CTD Sensors	29

CTD Fish	29

Primary Temperature	30

Secondary Temperature	31

Primary Conductivity	32

Secondary Conductivity	33

Primary Dissolved Oxygen	34

Secondary Dissolved Oxygen	35

Fluorometer	36

PAR	37

Transmissometer	38

MOCNESS Calibration Sheets	39

Pressure	39

Temperature	40

Conductivity	41

Transmissometer	42

Acquisition and Processing Information	43

Processing Specifics	43

Errors and Events	43

# Introduction

The LMG data acquisition systems continuously log data from a suite of instrumentation throughout the cruise.  This document describes the format of that data and its location on the distribution CDs.  It also contains important information that may affect how this data is processed such as instrument failures or other known problems with acquisition.

The data collected during this cruise is distributed on a CD-ROM written in ISO9660 level-1 format.  This data format has very strict requirements on filenames and organization.  However, it is readable by virtually every computing platform.

All of the data has been archived with the Unix “tar” command and/or compressed using Unix “gzip” compression.  Tar files have a “.tar” extension and Gzipped files have a “.gz” extension.  Tools are available on all platforms for uncompressing and de-archiving these formats.  On Macintosh, Stuffit Expander with DropStuff will open a tar archive and uncompress gzipped and Unix compressed files.  For Windows, WinZip, a shareware utility included on this CD (remember, it is shareware) will open these files.

In some cases to adhere to the ISO9660 format the .tar extension was removed.  When we tarred the files then gzip the tar archive the name of the file became File.tgz.  This name does not follow the 8.3 naming convention of the ISO9660 format.  On Windows and Mac Platforms Winzip and Stuffit Expander handles this just fine.  When they expand the File.gz the expanded file becomes File.tar, which both software packages can handle.  On Unix platforms gunzip expands File.tgz but it does not append the .tar extension.  So you may not recognize the file as a tar archive, but OS does recognize it as a tar archive.  If you use the file command it will return saying it is a tar file.  The below tar command will un-archive the file just fine.

IMPORTANT:  Read the last section in this document, Acquisition Problems and Events, for important information that may affect the processing of this data.

# Archive Data Extraction

It is often useful to know exactly how an archive was produced when expanding its contents.  Tar files were created using the following commands:

tar cvf archive-file files-to-be-archived

To create a list of the files in the archive:

tar tvf  archive-file  > contents.list

To extract the files from the archive:

tar xvf  archive-file file(s)-to-extract

G-zipped files will have a “.gz” extension on the filename. These files can be decompressed after de-archiving, using:

gunzip filename.gz

# CD Directory Structure

| ADCP: ADCP.tar Cal: InstCoef.txt CTD: Ctd.tar Imagery: Imag.tar Maps: Process: JGOF.tar PCO2.tar PROC.tar QC.tar Report: Report.doc RVDAS: nav/ uw/ Salinity: Logsheet.pdf Salts.xls Science: Utility: Acrobat Winzip XBT: Xbt.tar XCTD: Xctd.tar |  |  |
| --- | --- | --- |

# Distribution Contents

## ADCP

##### /Adcp/

This directory contains a tar file of gentoo’s proc directory, which contains a database of the averaged ping data, Matlab m-files used in processing the data, and daily graphs of the currents.  For more information contact Teri Chereskin at tchereskin@ucsd.edu .

## Calibration

##### /Cal/

Refer to the InstCoef.txt file along with the specific instrument calibration sheets, both located in this directory, for information on how the RVDAS data was collected and processed.

## Imagery

##### /Imagery/

This directory contains things such as ice imagery, isobar charts, sat imagery, wave and wind images, and weather reports.

## Data and Science Report

##### /Report/

Copies of this report in MS Word, HTML, and text formats.

## XBT

##### /XBT/

Contains a zip archive of XBT data generated for the Drake Transect by NOAA standard “AMVERSEAS” software.  Non-Drake transect data may also be included, which will a combination of binary and ascii files generated by standard Sippican MK-21 software.

## XCTD

##### /XCTD/

Contains binary and ascii data files as generated by standard Sippican MK-21 software.

## Logsheets

##### /logsheet/

This directory contains logsheets for XBT, XCTD, air samples and TCO2 data.  For further information on this data (TCO2), contact Tim Newberger at tnewberg@ldeo.columbia.edu.

## Salts

##### /Salinity/

This directory contains the log sheet for the Salt sample take during the Drake Transect Sampling, also a spreadsheet containing the Salt sample and TSG comparison.  These samples were analyzed with the onboard AutoSal by the MST.

## Science

##### /Science/

This directory, if populated, contains data specified by the on-board science party.

## Maps

##### /Maps/

This directory maps and mapping data generated by the ship’s MCIS and automated scripts, usually in JPEG or PostScript format, plus any maps provided for this purpose by the on-board science party.

## QC Plots

##### /QC_PLOTS/

Postscript files of data stored each day on RVDAS for quality control analysis during the cruise.  There are 3 types of files, named metXXX.ps, navXXX.ps, and oceanXXX.ps, where XXX is represents the Julian day.  Met files are a summary of the data from the meteorological instruments, Nav files are a summary of navigational data, and Ocean files are a summary of the underway seawater and bathymetry data.

## JGOFS Data Set

##### /JGOF/

The JGOFS data set consists of a single file produced each day named jg<julian_day>.dat.gz where <julian_day> is the day the data was acquired. The “.gz” extension indicates that the individual files are compressed before archiving. The daily file consists of 22 separate columnar fields in text format, which are described below. The JGOFS data set is obtained primarily by applying calibrations to raw data and decimating to whole minute intervals.  However, several fields are derived measurements from more than a single raw input.  Note: Null, unused, or unknown fields are filled with 9’s in the JGOFS data.

Additionally, 3 separate QC plots are generated daily by the ET using the JGOFS data set.  These plots include TSG and Bathymetry data, meteorological data, and navigation data.  The files are called ocean<julian_day>.ps, met<julian_day>.ps, and nav<julian_day>.ps respectively.

| Field | Data | Units |
| --- | --- | --- |
| 01 | GMT date | dd/mm/yy |
| 02 | GMT time | hh:mm:ss |
| 03 | PCOD latitude (negative is South) | Ddd.dddd |
| 04 | PCOD longitude (negative is West) | Ddd.dddd |
| 05 | Ships speed | Knots |
| 06 | GPS HDOP | - |
| 07 | Gyro Heading | Degrees (azimuth) |
| 08 | Course over ground | Degrees (azimuth) |
| 09 | Mast PAR | Einsteins/meters2 sec |
| 10 | Sea surface temperature | (C |
| 11 | Not used | - |
| 12 | Sea surface salinity | PSU |
| 13 | Sea depth (uncorrected, calc. sw sound vel. 1500 m/s) | meters |
| 14 | True wind speed (port windbird) | meters/sec |
| 15 | True wind direction (port windbird) | degrees (azimuth) |
| 16 | Ambient air temperature | (C |
| 17 | Relative humidity | % |
| 18 | Barometric pressure | mBars |
| 19 | Sea surface fluorometry | volts (0-5 FSO) |
| 20 | Not used | - |
| 21 | PSP | W/m2 |
| 22 | PIR | W/m2 |

## TSG Data files

##### /TSG/tsgfl

RVDAS processes the ltsg.d### file, using the Seabird calibration.  It produces a daily tsgfl.d### file with the below fields.

04+321:00:01:23.978 -00.070 -00.089 02.8042 33.75690 0.471306 4.341880

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | Internal water temperature | (C |
| 3 | External water temperature | (C |
| 4 | Conductivity | S/cm |
| 5 | Salinity | PSU |
| 6 | Transmissometer signal | Volts |

## RVDAS

##### /RVDAS/

RVDAS (Research Vessel Data Acquisition System) was developed at Lamont-Doherty Earth Observatory of Columbia University and has been used on the R/V Maurice Ewing for several years.  It was adapted for use on the Nathaniel B. Palmer and her sister ship, the R/V Laurence M. Gould.

Below you will find detailed information on the data included. Be sure to read the “Significant Acquisition Events” section below for important information about data acquisition during this cruise.

### Meteorological and Light Data

| Measurement | File ID | Collect. Status | Rate | Instrument |
| --- | --- | --- | --- | --- |
| Air Temperature | lmwx | continuous | 1 sec | R. M. young 41372VC |
| Relative Humidity | lmwx | continuous | 1 sec | R. M. young 41372VC |
| Wind Speed/Direction | lmwx | continuous | 1 sec | Gill Ultrasonic |
| PAR, (Photosynthetically- Available Radiation) | lmwx | continuous | 1 sec | BSI QSR-240 |
| Barometer | lmwx | continuous | 1 sec | R. M. young 61201 |
| GUV | lguv | continuous | 1 sec | GUV2511 |
| PIR (LW radiation) | lmwx | continuous | 1 sec | Eppley PIR |
| PSP (SW radiation) | lmwx | continuous | 1 sec | Eppley PSP |
| Port Ultrasonic Wind Speed/Direction | lmwx | continuous | 1 sec | Gill Wind Observer II |

### Navigational Data

| Measurement | File ID | Collect. Status | Rate | Instrument |
| --- | --- | --- | --- | --- |
| Trimble GPS | tgps | civilian mode | 1 sec | Trimble 20636-00SM |
| Gyro | lgyr | continuous | 0.2 sec | Anschutz Gyro |
| Garmin GPS | lgar | continuous | 1 sec | Garmin 17 |
| Seapath GPS | Lsep | Continuous | 1 sec | Seapath 330 |

### Geophysical Data

| Measurement | File ID | Collect. Status | Rate | Instrument |
| --- | --- | --- | --- | --- |
| Bathymetry | lknu | variable | Varies | Knudsen 320B/R |
| DUSH 11 Winch | lwn1 | variable | varies | Markey DUSH 11 |
| DUSH 5 Winch | lwn1 | variable | varies | Markey DUSH 5 |
| DUSH 4 Winch | lwn1 | variable | varies | Markey DUSH 4 |

### Oceanographic Data

| Measurement | File ID | Collect. Status | Rate | Instrument |
| --- | --- | --- | --- | --- |
| Salinity | utsg | continuous | 1 sec | SeaBird 45 |
| Sea Surface Temperature | Lrtm | continuous | 1 sec | SeaBird 38 |
| Fluorometry (digital) | lflr | continuous | 1 sec | Turner 10-AU-005 |
| Fluorometry (digital) | ldflr | continuous | 1 sec | Wetlab ECO |
| ADCP, Speed Log | ladc | continuous | 1 sec | RD Instruments |
| Oxygen | loxy | continuous | 1 sec |  |
| PCO2 | lpco2 | continuous | 2.5 min |  |

# Data File Names and Structures

RVDAS data is divided into two broad categories, Underway and Navigation.  The groups are abbreviated “uw” and “nav”. Thus, these two tar files, lmguw.tar and lmgnav.tar exist under the top-level rvdas directory. The instruments are broken down as shown. Each data file is g-zipped to save space on the distribution.  Not all data types are collected everyday or on every cruise.

RVDAS data files are named following the convention: LMG[FileID].dDDD.

The FileID is a 4-character code representing the system being logged, for example: lmet (for meteorology)

DDD is the Julian day of the data collection

| Underway Data | File ID |  | Navigation Data | File ID |
| --- | --- | --- | --- | --- |
| Meteorological - Cambell | lmwx |  | Gyro Compass | lgyr |
| Knudsen | lknu |  | P-CODE GPS | tgps |
| microTSG | utsg |  | Garmin 17 GPS | lgar |
| Digital Remote Temperature | lrtm |  | Seapath 330 GPS | lsep |
| Fluorometer – Wetlab ECO | ldfl |  |  |  |
| ADCP | ladc |  |  |  |
| Sound Velocity Probe | lsvp |  |  |  |
| GUV & PUV | lguv |  |  |  |
| PCO2 System | lpco |  |  |  |
| Oxygen | loxy |  |  |  |
| Wet Wall Flows | lsea |  |  |  |
| Winches: Dush4,5,&11 | lwn1 |  |  |  |
| Net Depth Sensor | lnds |  |  |  |

Data is received by the RVDAS system via RS-232 serial connections. The data files that comprise the rvdas data set are described below. A time tag is added to each line of data received and the data is written to disk.

YY+DDD:HH:MM:SS.SSS [data stream from instrument]

Where, YY: two-digit year, DDD: Julian Day, HH: 2 digit hours, MM: 2 digit minutes SS.SSS: seconds.  All times are UTC.

The delimiters used to separate fields in the raw data files are usually spaces and commas, but other delimiters are used (::, =, @) and occasionally there is no delimiter.  Care should be taken when reprocessing the data that the fields separations are clearly understood.  An example data

## lknu – Knudsen Sonar

08+024:07:36:36.245 HF,00.00, 000,0,LF,448.9,-026,1

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | HF – high frequency header (12 kHz) |  |
| 3 | HF - depth to surface | meters |
| 4 | HF - Echo Strength |  |
| 5 | HF – Depth Valid Flag |  |
| 6 | LF – low frequency header (3.5 kHz) |  |
| 7 | LF - depth to surface | meters |
| 8 | LF - Echo Strength |  |
| 9 | LF – Depth Valid Flag |  |

## lnds – Net Depth Sensor

99+099:00:18:19.775 V01 00199.8

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | V01 – Sensor 1 | label |
| 3 | Depth | meters |

## lwn1 - Winches

08+033:11:27:50.673 RD,DUSH-5,00111.63,00000000,-0000012,1938

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | Record Identifier, RD=Remote Data |  |
| 3 | Winch Indentifier, DUSH-X where X is 4, 5, or 11 |  |
| 4 | Tension | lbs |
| 5 | Speed | Meters/minute |
| 6 | Payout | meters |
| 7 | Checksum |  |

## lmwx	- Campbell Meteorological DAS

# 08+034:13:52:14.216 PUS,A,356,002.15,M,+332.28,+000.97,60,08

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | PUS tag – Port UltraSonic Anemometer |  |
| 3 | Unit Identification, A-Z |  |
| 4 | Port Wind Direction, degrees relative to Bow | deg |
| 5 | Port Wind Speed | m/s |
| 6 | Units, M=meters per second |  |
| 7 | Sound Speed | m/s |
| 8 | Sonic Temperature | (C |
| 9 | Status, 0=ok, 60=Heating Enabled & ok, Other value mean a fault |  |
| 10 | Check Sum |  |

# 08+034:13:52:14.216 SUS,A,356,002.15,M,+332.28,+000.97,60,08

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | SUS tag – Starboard UltraSonic Anemometer |  |
| 3 | Unit Identification, A-Z |  |
| 4 | Port Wind Direction, degrees relative to Bow | deg |
| 5 | Port Wind Speed | m/s |
| 6 | Units, M=meters per second |  |
| 7 | Sound Speed | m/s |
| 8 | Sonic Temperature | (C |
| 9 | Status, 0=ok, 60=Heating Enabled & ok, Other value mean a fault |  |
| 10 | Check Sum |  |

# 08+034:13:52:14.454 MET,12.22322,44.25706,-75,-25,-363.6365,2.332982,-0.08215196,278.6845, 279.2192,854.6198

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | MET tag |  |
| 3 | Power Supply Voltage | Volts |
| 4 | Enclosure Relative Humidity | % |
| 5 | Air Temp | ºC |
| 6 | Air Relative Humidity | % |
| 7 | PAR | mVolts |
| 8 | PSP Thermopile | mVolts |
| 9 | PIR Thermopile | mVolts |
| 10 | PIR Case Temperature | (K |
| 11 | PIR Dome Temperature | (K |
| 12 | Barometer | mBars |

## utsg – microTSG, Thermosalinograph

For further information on this data, check www.seabird.com for SBE 45 MicroTSG Thermosalinograph

08+037:13:45:57.596   2.6470,  3.03853,  33.8129, 1459.351

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | Internal water temperature | (C |
| 3 | Conductivity | S/m |
| 4 | Salinity | psu |
| 5 | Sound Velocity | m/s |

## lrtm – digital Remote Temperature

For further information on this data, check on www.seabird.com on SBE38 Digital Thermometer

08+037:13:47:17.841  2.2527

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | External water temperature | (C |

## ldflr – Fluorometer, Wetlab ECO

08+037:13:55:08.434 99/99/99    99:99:99        0.00    2585    73      543

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | Fluorometer Date | mm/dd/yy |
| 3 | Fluorometer Time | hh:mm:ss |
| 4 | Chlorophyll Signal | (g/l |
| 5 | Reference | (q |
| 6 | Counts – Chlorophyll Signal | Count |
| 7 | Thermistor |  |

## loxy - Oxygen

For further information on this data, contact Tim Newberger at tnewberg@ldeo.columbia.edu

04+117:23:57:23.504 MEASUREMENT	  3830	   380	Oxygen: 	   309.95	Saturation: 	    83.48	Temperature: 	    -1.35	DPhase: 	    33.41	BPhase: 	    32.22	RPhase: 	     0.00	BAmp: 	   262.09	BPot: 	   163.00	RAmp: 	     0.00	RawTem.: 	   694.92

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2-4 | Measurement ID, Model Number, Serial Number | alphanumeric |
| 5 | Oxygen heading | text |
| 6 | Oxygen Reading | Raw numeric |
| 7 | Saturation heading | text |
| 8 | Saturation Reading | Raw numeric |
| 9 | Temperature heading | text |
| 10 | Water Temperature | ºC |
| 11 | Dphase heading | text |
| 12 | Dphase | Raw numeric |
| 13 | Bphase heading | text |
| 14 | BPhase | Raw numeric |
| 15 | Rphase heading | text |
| 16 | Rphase | Raw numeric |
| 17 | Bamp heading | text |
| 18 | Bamp | Raw numeric |
| 19 | Bpot heading | text |
| 20 | Bpot | Raw numeric |
| 21 | Ramp heading | text |
| 22 | Ramp | Raw numeric |
| 23 | RawTem heading | text |
| 24 | RawTemp | Raw numeric |

## lpco – PCO2 system

For further information on this data, contact Tim Newberger at tnewberg@ldeo.columbia.edu

02+319:23:59:13.748 2002319.99851    7154.27     26.49    1033.6     325.79      6.74     329.3   53.76    0   Equil

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | Julian date file string | Julian |
| 3 | IR voltage reading | mV |
| 4 | Cell temperature | (C |
| 5 | Barometer | millibars |
| 6 | VCO2 | mL |
| 7 | Equilibrator temperature | (C |
| 8 | PCO2 | millibars |
| 9 | Gas flow | mL/min |
| 10 | Solenoid position ID | number |
| 11 | Valve Position ID | number |
| 12 | Measured gas | name |

## Lguv – Biospherical GUV

08+037:14:17:59.211 020608 141758 -.000099 1.307E0 7.24E0 1.316E1 2.609E1 3.285E1 3.505E1 8.075E-2 38.993 17.985

| GUV only | GUV and PUV |
| --- | --- |
| Field | Data | Units |  | Field | Data | Units |
| 1 | RVDAS Time Tag |  |  | 1 | RVDAS Time Tag |  |
| 2 | GUV Computer Date | mmddyy |  | 2 | GUV Computer Date | mmddyy |
| 3 | GUV Computer Time | hhmmss |  | 3 | GUV Computer Time | hhmmss |
| 4 | Ed0Gnd - GUV | Volts |  | 4 | EdZGnd -PUV | Volts |
| 5 | Ed0305 - GUV | μW/cm2nm |  | 5 | EdZ305 -PUV | μW/cm2nm |
| 6 | Ed0313 - GUV | μW/cm2nm |  | 6 | EdZ313 -PUV | μW/cm2nm |
| 7 | Ed0320 - GUV | μW/cm2nm |  | 7 | EdZ320 -PUV | μW/cm2nm |
| 8 | Ed0340 - GUV | μW/cm2nm |  | 8 | EdZ395 -PUV | μW/cm2nm |
| 9 | Ed0380 - GUV | μW/cm2nm |  | 9 | EdZ340 -PUV | μW/cm2nm |
| 10 | Ed0395 - GUV | μW/cm2nm |  | 10 | EdZPAR -PUV | μE/cm2sec |
| 11 | Ed0PAR - GUV | μE/cm2sec |  | 11 | LuZChl -PUV | μE/srm2sec |
| 12 | Ed0Temp - GUV | °C |  | 12 | EdZ380 -PUV | μW/cm2nm |
| 13 | Ed0VIn | Volts |  | 13 | WTemp -PUV | °C |
|  |  |  |  | 14 | Depth -PUV | m |
|  |  |  |  | 15 | EdZTemp -PUV | °C |
|  |  |  |  | 16 | LuZTemp -PUV | °C |
|  |  |  |  | 17 | Tilt -PUV | Degrees |
|  |  |  |  | 18 | Roll -PUV | Degrees |
|  |  |  |  | 19 | Ed0Gnd - GUV | Volts |
|  |  |  |  | 20 | Ed0305 - GUV | μW/cm2nm |
|  |  |  |  | 21 | Ed0313 - GUV | μW/cm2nm |
|  |  |  |  | 22 | Ed0320 - GUV | μW/cm2nm |
|  |  |  |  | 23 | Ed0340 - GUV | μW/cm2nm |
|  |  |  |  | 24 | Ed0380 - GUV | μW/cm2nm |
|  |  |  |  | 25 | Ed0395 - GUV | μW/cm2nm |
|  |  |  |  | 26 | Ed0PAR - GUV | μE/cm2sec |
|  |  |  |  | 27 | Ed0Temp - GUV | °C |
|  |  |  |  | 28 | Ed0VIn | Volts |

## lsvp -  Sound Velocity Probe in ADCP Transducer Well

00+348:01:59:52.128  1539.40

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | Sound velocity | m/s |

## ladc – ADCP Speed Log

00+019:23:59:59.099 $PUHAW,UVH,-1.48,-0.51,250.6

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $PUHAW |  |
| 3 | UVH (E-W, N-S, Heading) |  |
| 4 | Ship Speed relative to reference layer1 velocity2, East vector | knots |
| 5 | Ship Speed relative to reference layer1 velocity2, North vector | knots |
| 6 | Ship heading | degrees |

1The reference layer is an average velocity measured in a number of depth “bins”. On the LMG, the bins are eight meters deep and bins 3-10 define the reference layer. Hence, the reference layer is the water column from 16-80 meters beneath the ship.

2The speed ouput is water velocity relative to the ship’s hull and is therefore opposite of the actual

movement of the ship. For example, if the ship’s heading is due north, the North/South reference layer

velocity is likely to be negative (southerly).

## lgyr - Gyro

02+315:23:59:58.194 $PASVW,00.1,A*1D

02+315:23:59:58.414 $IIVHW,287.7,T,,M,,N,,K*71

02+315:23:59:58.616 $HEHDT,287.7,T*25

02+315:23:59:58.821 $HEROT,001.6,A*2C

02+315:23:59:58.984 $HCHDT,,T*07

##### HDT: True Heading

01+083:00:00:02.893 $HEHDT,246.3,T*2C

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag $HEHDT |  |
| 2 | Heading XXXXX = ddd.d | degrees |
| 3 | T flag for true heading, checksum |  |

##### ROT: Rate of Turn

01+083:00:00:03.093 $HEROT,-006.3,A*03

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag $HEROT |  |
| 2 | Rate of turn | degrees/min |
| 3 | Status: A = data valid, checksum |  |

## lsep – Seapath 330 GPS

##### INZDA: Time and Date Data

10+351:23:59:58.142 $INZDA,235958.08,17,12,2010,,*78

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $INZDA Tag |  |
| 3 | time | hhmmss.ss |
| 3 | day | dd |
| 4 | month | mm |
| 5 | year | yyyy |
| 6 | (blank) |  |
| 7 | Check sum | hexadecimal |

##### INGGA: Global Positioning Fix Data

10+351:23:59:58.142 $INGGA,235958.07,6118.168460,S,06008.089527,W,1,12,0.7,22.57,M,17.79,M,,*46

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $INGGA Tag |  |
| 3 | Time (UTC) | hhmmss.ss |
| 3 | Latitude in degrees with decimal minutes | ddmm.mmm |
| 4 | {N¦S} (latitude is north or south) |  |
| 5 | Longitude in degrees with decimal minutes | ddmm.mmm |
| 6 | {E¦W} (longitude is east of west) |  |
| 7 | GPS quality indicator: 0 = invalid position, 1 = GPS SPS used, 2 = DGPS used, 3 = GPS PPS used, 4 = GPS RTK used, 5 = GPS float RTK used, 6 = dead reckoning |  |
| 8 | Number of Satellites in use (00-99) |  |
| 9 | HDOP |  |
| 10 | Height above ellipsoid in meters | m.mm |
| 11 | M |  |
| 12 | Age of DGPS corrections in seconds | ss.ss |
| 13 | M |  |
| 14 | (blank) |  |
| 15 | *Check sum | hexadecimal |

##### INRMC: Recommended Minimum Specific GNSS Data

10+351:23:59:58.200 $INRMC,235958.07,A,6118.168460,S,06008.089527,W,12.8,331.22,171210,11.3,E,A*1C

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $INRMC Tag |  |
| 3 | UTC of position | hhmmss.ss |
| 4 | Status A = Data Valid, V = Navigation Receiver Warning |  |
| 5 | Latitude in degrees with decimal minutes | ddmm.mmm |
| 6 | North (N) or South (S) |  |
| 7 | Longitude in degrees with decimal minutes | ddmm.mmm |
| 8 | East (E) or West (W) |  |
| 9 | Speed Over Ground, knots | knots |
| 10 | Course Over Ground, degrees True | degrees |
| 11 | Date | ddmmyy |
| 12 | Magnetic Variation, degrees E/W | degrees |
| 13 | Mode Indicator E= Estimated Mode |  |
| 14 | *Check sum |  |

##### PSXN,20: Data Quality

10+351:23:59:58.200 $PSXN,20,1,2,0,0*38

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $PSXN Tag |  |
| 3 | 20 (PSXN identifier) |  |
| 3 | Horizontal position and velocity quality: 0 = normal, 1 = reduced performance, 2 = invalid data |  |
| 4 | Height and vertical velocity quality: 0 = normal, 1 = reduced performance, 2 = invalid data |  |
| 5 | Heading quality: 0 = normal, 1 = reduced performance, 2 = invalid data |  |
| 6 | Roll and pitch quality: 0 = normal, 1 = reduced performance, 2 = invalid data |  |
| 7 | *Check sum | hexadecimal |

##### PSXN,23: Roll, Pitch, Heading and Heave

10+351:23:59:58.213 $PSXN,23,0.02,-0.76,330.56,*0B

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $PSXN Tag |  |
| 3 | 23 (PSXN identifier) |  |
| 3 | Roll in degrees. Positive with port side up. | d.dd |
| 4 | Pitch in degrees. Positive with bow up. | d.dd |
| 5 | Heading in degrees true | d.dd |
| 6 | Heave in meters. Positive is down | m.mm |
| 7 | *Check sum | hexadecimal |

## lgar - Garmin GPS

##### GGA: Global Positioning Fix Data

08+034:12:26:06.131 $GPGGA,122607,6446.4733,S,06403.4455,W,1,11,0.9,-193.4,M,9.7,M,,*5A

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $GPGGA Tag |  |
| 3 | UTC of position | hhmmss.ss |
| 4 | Latitude in degrees with decimal minutes | ddmm.mmm |
| 5 | North (N) or South (S) |  |
| 6 | Longitude in degrees with decimal minutes | ddmm.mmm |
| 7 | East (E) or West (W) |  |
| 8 | GPS quality (1=GPS 2=DGPS) |  |
| 9 | Number of GPS satellites used |  |
| 10 | Horizontal dilution of precision (HDOP) |  |
| 11 | Antenna height above/below mean-sea-level (geoid) | meters |
| 12 | Units for antenna height (M = Meters) |  |
| 13 | Geoidal Separation1 |  |
| 14 | Units for Geoidal Separation (M = Meters) | meters |
| 15 | Age of differential GPS data, number of seconds since last SC104 Type 1 or 9 |  |
| 16 | Differential reference station ID |  |

1Geoidal Separation: the difference between the WGS-84 earth ellipsoid and mean-sea-level (geoid). A negative value represents mean-sea-level below ellipsoid.

##### GLL: Geographic Position – Latitiude/Logitude

08+034:12:26:06.211 $GPGLL,6446.4733,S,06403.4455,W,122607,A

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $GPGLL Tag |  |
| 3 | Latitude | ddmm.mmm |
| 4 | North (N) or South (S) |  |
| 5 | Logitude | ddmm.mmm |
| 6 | East (E) or West (W) |  |
| 7 | UTC of position | hhmmss.ss |
| 8 | Status: A = Data Valid, V =Data Not Valid |  |

##### VTG: Track Made Good and Speed over Ground

08+034:12:26:06.211 $GPVTG,167,T,151,M,000.0,N,0000.0,K

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $GPVTG Tag |  |
| 3 | Track, degrees true | degrees |
| 3 | T flag for True |  |
| 4 | Track, degrees magnetic | degrees |
| 5 | M flag for Magnetic |  |
| 6 | Speed over Ground | knots |
| 7 | N flag for Knots |  |
| 8 | Speed over Ground | kmhr |
| 9 | K flag for km/hr |  |

## tgps – Trimble Centurion GPS

##### GGA: Global Positioning Fix Data

08+034:12:26:06.131 $GPGGA,122607,6446.4733,S,06403.4455,W,1,11,0.9,-193.4,M,9.7,M,,*5A

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $GPGGA Tag |  |
| 3 | UTC of position | hhmmss.ss |
| 4 | Latitude in degrees with decimal minutes | ddmm.mmm |
| 5 | North (N) or South (S) |  |
| 6 | Longitude in degrees with decimal minutes | ddmm.mmm |
| 7 | East (E) or West (W) |  |
| 8 | GPS quality (1=GPS 2=DGPS) |  |
| 9 | Number of GPS satellites used |  |
| 10 | Horizontal dilution of precision (HDOP) |  |
| 11 | Antenna height above/below mean-sea-level (geoid) | meters |
| 12 | Units for antenna height (M = Meters) |  |
| 13 | Geoidal Separation1 |  |
| 14 | Units for Geoidal Separation (M = Meters) | meters |
| 15 | Age of differential GPS data, number of seconds since last SC104 Type 1 or 9 |  |
| 16 | Differential reference station ID |  |

1Geoidal Separation: the difference between the WGS-84 earth ellipsoid and mean-sea-level (geoid). A negative value represents mean-sea-level below ellipsoid.

##### GLL: Geographic Position – Latitiude/Logitude

08+034:12:26:06.211 $GPGLL,6446.4733,S,06403.4455,W,122607,A

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $GPGLL Tag |  |
| 3 | Latitude | ddmm.mmm |
| 4 | North (N) or South (S) |  |
| 5 | Logitude | ddmm.mmm |
| 6 | East (E) or West (W) |  |
| 7 | UTC of position | hhmmss.ss |
| 8 | Status: A = Data Valid, V =Data Not Valid |  |

##### VTG: Track Made Good and Speed over Ground

08+034:12:26:06.211 $GPVTG,167,T,151,M,000.0,N,0000.0,K

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $GPVTG Tag |  |
| 3 | Track, degrees true | degrees |
| 3 | T flag for True |  |
| 4 | Track, degrees magnetic | degrees |
| 5 | M flag for Magnetic |  |
| 6 | Speed over Ground | knots |
| 7 | N flag for Knots |  |
| 8 | Speed over Ground | kmhr |
| 9 | K flag for km/hr |  |

##### RMC: Recommended Minimum Specific GNSS Data

08+034:13:17:26.627 $GPRMC,131726.605,A,6446.4820,S,06403.3075,W,000.0,094.4,030208,16.3,E

| Field | Data | Units |
| --- | --- | --- |
| 1 | RVDAS Time Tag |  |
| 2 | $GPRMC Tag |  |
| 3 | UTC of position | hhmmss.ss |
| 4 | Status A = Data Valid, V = Navigation Receiver Warning |  |
| 5 | Latitude in degrees with decimal minutes | ddmm.mmm |
| 6 | North (N) or South (S) |  |
| 7 | Longitude in degrees with decimal minutes | ddmm.mmm |
| 8 | East (E) or West (W) |  |
| 9 | Speed Over Ground, knots | knots |
| 10 | Course Over Ground, degrees True | degrees |
| 11 | Date | ddmmyy |
| 12 | Magnetic Variation, degrees E/W | degrees |
| 13 | Mode Indicator E= Estimated Mode |  |

# LMG Sensors

## Shipboard Sensors

| Sensor | Description | Serial # | Cal. Date | Status |
| --- | --- | --- | --- | --- |
| Port Anemometer | Gill Ultrasonic Wind Observer II | 840019 | N/A | Collected |
| Starboard Anemometer | Gill Ultrasonic Wind Observer II | 71738 | N/A | Collected |
| Barometer | R.M. Young 61201 | BP0873 | 28-Jul-2010 | Collected |
| Humidity/Wet Temp | RM Young 41372LC | 06720 | 11-Feb-2010 | Collected |
| PAR for Mast | Biosph. Inst. QSR-240P | 6393 | 31-Aug-2010 | Collected |
| PIR | Eppley PIR | 28903F3 | 13-Oct-2010 | Collected |
| PSP | Eppley PSP | 28933F3 | 9-Sept-2010 | Collected |
| GUV (Mast) | Biosph. Inst. GUV-2511 | 25110805127 | 17-May-2010 | Collected |
| Transmissometer | WET Labs C-Star 25 cm deep | CST-553DR | 26-Aug-2010 | Collected |
| MicroTSG | Sea-Bird 45 | 243 | 21-Jul-2010 | Collected |
| Digital Remote Temp | Sea-Bird 38 | 324 | 26-Jan-2010 | Collected |
| Fluorometer | WET Labs ECO-FL | FLRTD-399 | 15-Sep-09 | Collected |

## CTD Sensors

| Sensor | Description | Serial # | Cal. Date | Status |
| --- | --- | --- | --- | --- |
| CTD Fish | Seabird SBE9Plus | 0232 | 01-Apr-10 | Collected |
| Primary Temperature | Seabird SBE3 | 2470 | 28-Apr-11 | Collected |
| Secondary Temperature | Seabird SBE3 | 2205 | 28-Apr-10 | Collected |
| Primary Conductivity | Seabird SBE4 | 2048 | 01-Apr-11 | Collected |
| Secondary Conductivity | Seabird SBE4 | 2065 | 21-Apr-10 | Collected |
| Primary Dissolved Oxygen | Seabird SBE43 | 0182 | 03-May-11 | Collected |
| Secondary Dissolved Oxygen | Seabird SBE43 | 0201 | 06-Jul-11 | Collected |
| Fluorometer | Wet Labs ECO | FLRTD-1735 | 14-Apr-11 | Collected |
| PAR | Biosph. Inst. QSP-2300 | 4722 | 19-May-10 | Collected |
| Transmissometer | Wet Labs C-Star | CST-406DR | 22-Mar-11 | Collected |

## MOCNESS Sensors

| Sensor | Description | Serial # | Cal. Date | Status |
| --- | --- | --- | --- | --- |
| Pressure | MOCNESS Depth Sensor | 156 | N/A | Collected |
| Temperature | Seabird SBE3 | 1619 | 20-Mar-09 | Collected |
| Conductivity | Seabird SBE4 | 2293 | 04-Mar-11 | Collected |
| Transmissometer | Wet Labs C-Star | CST-407DR | 22-Mar-11 | Collected |

# Underway Calibration Sheets

Note: Embedded pdf files can be opened with a right-click, Acrobat Document Object, Open

## Remote Temperature

Thermosalinograph

Transmissometer

Fluorometer

## PSP

PIR

## PAR

## Temperature/Relative Humidity

Barometer

GUV

# CTD Sensors

## CTD Fish

## Primary Temperature

## Secondary Temperature

## Primary Conductivity

## Secondary Conductivity

## Primary Dissolved Oxygen

## Secondary Dissolved Oxygen

## Fluorometer

## PAR

## Transmissometer

# MOCNESS Calibration Sheets

## Pressure

## Temperature

## Conductivity

## Transmissometer

# Acquisition and Processing Information

## Processing Specifics

Refer to the InstCoef.txt file along with the specific instrument calibration sheets, both located in the Cal/ directory of the data distribution, for information on how the RVDAS data was collected and processed.

## Errors and Events

This section lists all significant events and known problems with acquisition during this cruise including instrument failures, data acquisition system failures, and other factors affecting this data set.

The PCO2 system was turned off when it was discovered that there was no regulator onboard for the Chilean replacement Nitrogen tank. Palmer Station supplied the LMG with an appropriate tank for running the PCO2 system during the Northbound Drake passage.

| Date (Julian) | Time (GMT) | Event | Location |
| --- | --- | --- | --- |
| 307 | 03:00 | Started data collection. Trimble GPS not functioning | @68W |
| 308 |  | Turned off bottom tracking ADCP |  |
| 311 | 22:09 | Suspended water sampling and sonars. | Arrive Palmer Station |
| 313 | 09:49 | Resumed seawater and sonars | Departing Palmer Station |
| 313 | 12:01 | Turned on bottom tracking ADCP |  |
| 320 | 22:00 | PCO2 system turned off |  |
| 330 | 10:09 | Suspended water sampling and sonars. | Arrive Palmer Station |
| 331 | 10:09 | Resumed seawater and sonars | Departing Palmer Station |
| 335 | 02:35 | End data collection | @68W |